## Slide 1: Chapter 4:
Basic Computer Organization and Design
Topics to be covered:
Instruction Codes
Addressing modes
Computer Registers
Instruction Set
Timing and Control
Instruction Cycle
Memory Reference Instructions
Input –output devices
Design of Basic Computer
1

## Slide 2: 3-1 Instruction Codes
An instruction is a binary code that specifies a sequence of micro-operations.
Instructions are encoded as binary instruction codes.
Instruction codes and data are stored in memory
An instruction code is a group of bits that tells the computer to perform a specific operation part.
The computer reads each instruction from memory and places it
in a control register
The control unit interprets the binary code of the instruction and proceeds to execute it by issuing a sequence of micro-operations
An instruction is divided into parts (basic part is the operation
part)
– The operation code (op code) of an instruction is a group of bits that define operations such as add, subtract, multiply, shift and compliment.

## Slide 3: 4-1 Instruction Codes cont.
Instruction codes and data are stored in memory
The computer reads each instruction from memory and places it in a control register
The control unit interprets the binary code of the instruction and proceeds to execute it by issuing a sequence of micro- operations
An Instruction code is a group of bits that instructs the computer to perform a specific operation (sequence of microoperations such as add, subtract, shift, and complement).
Instruction code is divided into parts (basic part is the operation part)

## Slide 4: 4-1 Instruction Codes cont.
110010??????????
Op code
Control
Unit
Read instruction
from memory
Memory
Suppose we are having 64 operation then the length of OpCode will be 6. (since 26=64)
The control unit decode the OpCode and determines the operations
It’s an ADD
operation
The number of bits required for the operation code depends on the total number of operations available in the computer
n bit operation code -> 2n (or little less) distinct operations
  It must consist of at least n bits for a given 2n distinct operations

## Slide 5: 4-1 Instruction Codes cont.
An operation must be performed on some data stored in processor registers or in memory
An instruction code must therefore specify not only the operation, but also the location of the operands (in registers or in the memory), and where the result will be stored (registers/memory)
Memory words can be specified in instruction codes by their address

## Slide 6: 4-1 Instruction Codes cont.
Every Computer has its own particular instruction code format.
– Instruction code formats are conceived by computer
designers who specify the architecture of the computer
The simplest way to organize a computer is to have Processor Register and instruction code with two parts.
The ﬁrst part speciﬁes the operation to be performed and the second speciﬁes an address
Instruction Format
The first part specifies the operation to be performed and second specifies an address.
The memory address tells where the operand in memory will be found.
Opcode
Address
15 12 11
0
What to do: Opcode Where: memory address

## Slide 7: 4-1 Instruction Codes
Opcode
Address
Instruction Format
Binary Operand
Operands
(data)
Processor register (Accumulator AC)
Memory 4096x16
15 12 11
0
15
0
Instructions
(program)
15 0
0
15
212=4096 word of RAM , 12 bits are required for addressing
16 bit RAM (word length)

## Slide 8: 4-2 Addressing modes
The operation field of an instruction specifies the operation to be performed.
This operation will be executed on some data which is stored in computer registers or the main memory.
The way any operand is selected during the program execution is dependent on the addressing mode of the instruction.
  Addressing mode refers to the way in which the operand of an instruction is specified.
There are different Addressing Modes used for address portion of the instruction code. Some of these addressing modes are
  Immediate addressing mode
  Direct addressing mode
  Indirect addressing mode

## Slide 9: 4-2 Addressing modes
Immediate: it specifies the actual operand.
the operand is given in the address portion (constant)
  For example: ADD 7
    which says Add 7 to contents of accumulator. 7 is the operand here.
Direct: it specifies the address of the operand.
the address points to the operand stored in the memory
  effective address of operand is present in instruction itself.
  Single memory reference to access data.
  No additional calculations to find the effective address of the operand.

## Slide 10: 4-2 Addressing modes
Indirect: it specifies the address of memory word in which address of operand is found.
the address points to the pointer (another address) stored in the memory that references the operand in memory – This slows down the execution, as this includes multiple
memory lookups to find the operand.
One bit of the instruction code can be used to distinguish between direct & indirect addresses

## Slide 11: 4-2 Addressing modes
Opcode
Address
Instruction Format
15 14
I
12 11 0
0
ADD
457
22
Operand
457
1
35
1350
300
Operand
1350
+
AC
+
AC
Direct Address
Indirect address
ADD 300
Effective address
Effective address: the address of the operand
The addressing mod (I) is 0 for direct addressing and 1 for indirect mode in the following instruction format.

## Slide 12: In order to cover the basic concepts behind designing a computer, a model (an imaginary system) will be presented to you throughout this chapter. This model will be called the “Basic Computer”
The basic computer has 8 registers, a memory unit
and a control unit.
A Common Bus System is used for transferring data in a system.
The basic computer has three instruction code formats.

## Slide 13: 4-3 Computer Registers
Computer instructions are normally stored in consecutive memory locations and executed sequentially one at a time
The control reads an instruction from a specific address in memory and executes it, and so on
This type of sequencing needs a counter to calculate the address of the next instruction after execution of the current instruction is completed
It is also necessary to provide a register in the control unit for storing the instruction code after it is read from memory
The computer needs processor registers for manipulating data and a register for holding a memory address

## Slide 14: Registers in the Basic Computer
List of BC Registers
DR | 16 | Data Register | Holds memory operand
AR | 12 | Address Register | Holds address for memory
AC | 16 | Accumulator | Processor register
IR | 16 | Instruction Register | Holds instruction code
PC | 12 | Program Counter | Holds address of instruction
TR | 16 | Temporary Register | Holds temporary data
INPR | 8 | Input Register | Holds input character
OUTR | 8 | Output Register | Holds output character
11 0
PC
15
0
IR
15 0
TR
7 0 7 0
OUTR
15 0
DR
15 0
AC
11 0
AR
INPR
Memory 4096 x 16

## Slide 15
S2
S1
S0
Bus
LD INR CLR
Address
Memory unit 4096 x 16
Write Read
AR
LD INR CLR
PC
LD INR CLR
DR
AC
LD INR CLR
Adder
and
logic
E
INPR
IR
LD
TR
LD INR CLR
OUTR
LD
Clock
16-bit common bus
7
1
2
3
4
5
6
Computer Registers Common Bus System
Register  Memory: Write operation
M[AR]  DR
Memory  Register: Read operation
DR  M[AR]
IR←M[AR]
(note that AC cannot directly read from memory!!)
Bus is a set of wires in a computer along which information can be sent to and from
other parts of the computer

## Slide 16: 4-3 Computer Registers Common Bus System cont.
Bus is a communication pathway connecting two or more devices.
S2S1S0: Selects the register/memory that would use the bus
LD (load): When enabled, the particular register receives the data
from the bus during the next clock pulse transition
E (extended AC bit): flip-flop holds the carry
DR, AC, IR, and TR: have 16 bits each
AR and PC: have 12 bits each since they hold a memory address
When the contents of AR or PC are applied to the 16-bit common bus, the four most significant bits are set to zeros
When AR or PC receives information from the bus, only the 12
least significant bits are transferred into the register
INPR and OUTR: communicate with the eight least significant bits in the bus

## Slide 17: 4-3 Computer Registers Common Bus System cont.
INPR: Receives a character from the input device (keyboard,…etc) which is then transferred to AC
OUTR: Receives a character from AC and delivers it to an output device (say a Monitor)
Five registers have three control inputs:
i.e. LD (load), INR (increment), and CLR (clear)
The input data and output data of the memory are connected to the common bus
But the memory address is connected to AR
Therefore, AR must always be used to specify a memory address

## Slide 18: 4-3 Computer Registers cont.
The transition at the end of the cycle transfers the content of the bus into the destination register, and the output of the adder and logic circuit into the AC
For example, the two microoperations
DR←AC and AC←DR can be executed at the same time
This is done by:
(Exchange)

## Slide 19: 4-3 Computer Registers cont.
1- place the contents of AC on the bus (S2S1S0=100)
2- enabling the LD (load) input of DR
3- Transferring the contents of the DR through the adder and logic circuit into AC
4- enabling the LD (load) input of AC
All during the same clock cycle
The two transfers occur upon the arrival of the clock pulse transition at the end of the clock cycle

## Slide 20: 4-4 Instruction Set
Computer instructions are a set of machine language instructions that a particular processor understands and executes.
A computer performs tasks on the basis of the instruction provided.
What is instruction set?
  An instruction set is a list of commands ready to be executed directly by CPU.
  The entire group of instructions that a microprocessor supports is called Instruction Set.
  It is the complete set of all the instructions in machine code that can be recognized and executed by a central
processing unit.
NB: Each computer has its unique instruction set
  Eg., Intel Microprocessor 8085 has 246 instructions

## Slide 21: 4-4 Instruction Set
Instruction Set Completeness
The set of instructions are said to be complete if the computer includes a sufficient number of instructions in each of the following categories:
  Arithmetic, logical, and shift instructions
  Instructions for moving information to and from memory and processor registers
  Program control instructions together with instructions that check status conditions
  Input & output instructions

## Slide 22: 4.4 Instruction Classification
Computer provides an extensive set of instructions to give the user the flexibility to carryout various computational task.
Most computer instruction can be classified into three categories.
  Data transfer instruction
  Data manipulation instruction
  Program control instruction
1. Data Transfer Instruction
used to move data from one place in the computer to another
without changing the data content.
The most common transfers are: between memory and processes registers, between processes register & input or output, and between processes register themselves

## Slide 23: 4.4. Instruction Classification
Load Store Move Exchange Input Output Push
Pop
LD ST MOV XCH IN OUT PUSH POP
Typical Data Transfer Instructions
Name Mnemonic
Data Manipulation Instruction
  It performs operations on data and provides the computational capabilities for the computer.
  The data manipulation instructions in a typical computer are usually divided into three basic types.
    Arithmetic Instruction
    Logical bit manipulation Instruction
    Shift Instruction.

## Slide 24: 3.6 Instruction Classification
Arithmetic Instructions
Clear Complement AND
OR
Exclusive-OR Clear carry Set carry
CLR COM AND OR XOR CLRC SETC
Complement carry COMC Enable interrupt EI Disable interrupt DI
Logical and Bit Manipulation Instructions
Name Mnemonic
Name | Mnemonic
Increment | INC
Decrement | DEC
Add | ADD
Subtract | SUB
Multiply | MUL
Divide | DIV
Add with Carry | ADDC
Subtract with Borrow | SUBB
Negate(2’s Complement) | NEG
Name | Mnemonic
Logical shift right | SHR
Logical shift left | SHL
Arithmetic shift right | SHRA
Arithmetic shift left | SHLA
Rotate right | ROR
Rotate left | ROL
Rotate right thru carry | RORC
Rotate left thru carry | ROLC
Shift Instructions

## Slide 25: 3.6 Instruction Classification
Examples of Program Control Instructions
Program control instructions specify conditions for altering the
content of the program counter, while data transfer and manipulation instructions specify conditions for data processing operations.
Name | Mnemonic
Branch | BR
Jump | JMP
Skip | SKP
Call | CALL
Return | RTN
Compare(by - ) | CMP
Test (by AND) | TST
3. Program Control Instructions

## Slide 26: 4-4 Computer Instructions
The basic computer has three Instruction code formats
Each format has 16 bits
Memory-Reference Instructions (OP-code = 000 ~ 110)
15 14 12 11 0
I | Opcode | Address
(OP-code = 111, I = 0)
0
Register-Reference Instructions
15 12 11
0 1 1 1 Register operation
(OP-code =111, I = 1)
0
Input-Output Instructions
15 12 11
1 1 1 1 I/O operation

## Slide 27: BASIC COMPUTER INSTRUCTIONS
Symbol | Hex Code I = 0 I = 1 | Description
AND ADD LDA STA BUN BSA ISZ | 0xxx 8xxx 1xxx 9xxx 2xxx Axxx 3xxx Bxxx 4xxx Cxxx 5xxx Dxxx 6xxx Exxx | AND memory word to AC Add memory word to AC Load AC from memory Store content of AC into memory Branch unconditionally Branch and save return address Increment and skip if zero
CLA CLE CMA CME CIR CIL INC SPA SNA SZA SZE HLT | 7800 7400 7200 7100 7080 7040 7020 7010 7008 7004 7002 7001 | Clear AC Clear E Complement AC Complement E Circulate right AC and E Circulate left AC and E Increment AC Skip next instr. if AC is positive Skip next instr. if AC is negative Skip next instr. if AC is zero Skip next instr. if E is zero Halt computer
INP OUT SKI SKO ION IOF | F800 F400 F200 F100 F080 F040 | Input character to AC Output character from AC Skip on input flag Skip on output flag Interrupt on Interrupt off
Memory-Reference Instructions
Register -Reference Instructions
I/O
Instructions

## Slide 28: 4-4 Computer Instructions
Instruction Set Completeness
The set of instructions are said to be complete if the computer includes a sufficient number of instructions in each of the following categories:
  Arithmetic, logical, and shift instructions
  Instructions for moving information to and from
memory and processor registers
  Program control instructions together with instructions that check status conditions
  Input & output instructions

## Slide 29: 4-5 Timing & Control
The timing for all registers in the basic computer is controlled by a master clock generator
The clock pulses are applied to all flip-flops and registers in the system, including the flip-flops and registers in the control unit
The clock pulses do not change the state of a register unless the register is enabled by a control signal (i.e., Load)

## Slide 30: 4-5 Timing & Control cont.
The control signals are generated in the control unit and provide control inputs for the multiplexers in the common bus, control inputs in processor registers, and microoperations for the accumulator
There are two major types of control organization:
  Hardwired control
  Microprogrammed control

## Slide 31: 4-5 Timing & Control cont.
In the hardwired organization, the control logic is implemented with gates, flip-flops, decoders, and other digital circuits.
In the microprogrammed organization, the control information is stored in a control memory (if the design is modified, the microprogram in control memory has to be updated)
Microprogrammed control unit
  Is less complex and simpler to implement than hardwired control unit
  Hence, it is cheaper and less error prone than hardwired control unit
  But it is slower than hardwired control unit

## Slide 32: The Control Unit for the basic computer
I
Hardwired Control Organization
Instruction register (IR)
15
14 13 12
11 - 0
3 x 8 decoder
7 6 5 4 3 2 1 0
Control
logic gates
D0
15 14 . . . . 2 1 0
4 x 16
Sequence decoder
4-bit sequence counter (SC)
Increment (INR) Clear (CLR)
Clock
Other inputs
Control outputs
D7
T15
T0

## Slide 33: Timing signals Generated by 4-bit sequence counter and 4x16 decoder The SC can be incremented or cleared.
- Example: T0, T1, T2, T3, T4, T0, T1, . . .
Assume: At time T4, SC is cleared to 0 if decoder output D3 is active.
D3T4: SC  0
T0 T1 T2 T3 T4 T0
Clock
T0 T1 T2 T3 T4 D3
CLR SC

## Slide 34: 4-5 Timing & Control cont.
T0: AR←PC
  Transfers the content of PC into AR if timing signal T0 is active
  T0 is active during an entire clock cycle interval
  During this time, the content of PC is placed onto the bus (with S2S1S0=010) and the LD (load) input of AR is enabled
  The actual transfer does not occur until the end of the clock cycle when the clock goes through a positive transition
  This same positive clock transition increments the sequence counter SC from 0000 to 0001
  The next clock cycle has T1 active and T0 inactive

## Slide 35: 4-6 Instruction Cycle
A program is a sequence of instructions stored in memory
The program is executed in the computer by going through a cycle for each instruction (in most cases)
Each instruction in turn is subdivided into a sequence of sub-cycles or phases

## Slide 36: 4-6 Instruction Cycle cont.
Instruction Cycle Phases:
  1- Fetch an instruction from memory
  2- Decode the instruction
  3- Read the effective address from memory if the instruction has an indirect address
  4- Execute the instruction
This cycle repeats indefinitely unless a HALT instruction is encountered

## Slide 37: 4-6 Instruction Cycle Fetch and Decode
Initially, the Program Counter (PC) is loaded with the address of the first instruction in the program
The sequence counter SC is cleared to 0, providing a decoded timing signal T0
After each clock pulse, SC is incremented by one, so that the timing signals go through a sequence T0, T1, T2, and so on

## Slide 38: 4-6 Instruction Cycle Fetch and Decode cont.
T0: AR←PC (this is essential!!)
The address of the instruction is moved to AR.
T1: IR←M[AR], PC←PC+1
The instruction is fetched from the memory to IR
,and the PC is incremented.
T2: D0,…, D7←Decode IR(12-14), AR←IR(0- 11), I←IR(15)

## Slide 39
= 0 (direct)
D'7IT3: D'7I'T3: D7I'T3: D7IT3:
AR  M[AR]
Nothing
Execute a register-reference instr. Execute an input-output instr.
Start
SC  
AR  PC
T0
IR  M[AR], PC  PC + 1
T1
Decode Opcode in IR(12-14), AR  IR(0-11), I  IR(15)
T2
D7
(Register or I/O) = 1 = 0 (Memory-reference)
I
I
Execute register-reference
instruction
SC  0
Execute input-output instruction
SC  0
AR  M[AR]
Nothing
(I/O) = 1 = 0 (register) (indirect) = 1
T3 T3
T3
T3
Execute memory-reference
instruction
SC  0
T4
DETERMINE THE TYPE OF INSTRUCTION

## Slide 40: MEMORY REFERENCE INSTRUCTIONS
Read operand AND with AC
D0T4: DR  M[AR]
D0T5: AC  AC  DR, SC  0 ADD to AC
D1T4: DR  M[AR]
D1T5: AC  AC + DR, E  Cout, SC  0
The effective address of the instruction is in AR and was placed there during timing signal T2 when I = 0, or during timing signal T3 when I = 1
The execution of MR Instruction starts with T4
AND to AC
Read operand
Add to AC and store carry in E
Symbol | Operation Decoder | Symbolic Description
AND ADD LDA STA BUN BSA ISZ | D0 D1 D2 D3 D4 D5 D6 | AC  AC  M[AR] AC  AC + M[AR], E  Cout AC  M[AR] M[AR]  AC PC  AR M[AR]  PC, PC  AR + 1 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1

## Slide 41: 4-7 Input-Output Devices
Instructions and data stored in memory must come from some input devices
Computational results must be transmitted to the user through some output device
For the system to communicate with an input device, serial information is shifted into the input register INPR
To output information, it is stored in the output register OUTR

## Slide 42: 4-7 Input-Output Devices
Input-output
terminal
Serial
communication interface
registers and
Computer flip-flops
Printer
Keyboard
Receiver interface
Transmitter interface
FGO
OUTR
AC
INPR
FGI
Serial Communications Path Parallel Communications Path

## Slide 43: 4-7 Input-Output Devices cont.
INPR and OUTR communicate with a communication interface serially and with the AC in parallel. They hold an 8-bit alphanumeric information
I/O devices are slower than a computer system  we need to synchronize the timing rate difference between the input/output device and the computer.
FGI: 1-bit input flag (Flip-Flop) aimed to control the input operation

## Slide 44: 4-7 Input-Output Devicescont.
FGI is set to 1 when a new information is available in the input device and is cleared to 0 when the information is accepted by the computer
FGO: 1-bit output flag used as a control flip-flop to control the output operation
If FGO is set to 1, then this means that the computer can send out the information from AC. If it is 0, then the output device is busy and the computer has to wait!

## Slide 45: 4-8 Design of Basic Computer
A memory unit: 4096 x 16.
Registers: AR, PC, DR, AC, IR, TR, OUTR, INPR,
and SC
Flip-Flops (Status): I, E, FGI, and FGO
Decoders:
  a 3x8 Opcode decoder
  a 4x16 timing decoder
Common bus: 16 bits
Control logic gates
Adder and Logic circuit: Connected to AC

## Slide 46: 4-8 Design of Basic Computercont.
The control logic gates are used to control:
  Inputs of the nine registers
  Read and Write inputs of memory
  Set, Clear, or Complement inputs of the flip- flops
  S2, S1, S0 that select a register for the bus
  AC Adder and Logic circuit