## Slide 2: IPV6(cont’d..)
IPv6 addresses are 128-bit
There are no checksum bits
There is Stateless address autoconfiguration in IPv6: – Hosts autoconfigure themselves with IPv6 addresses.
There is no need for NAT, since each device in an IPV6 network has a globally unique IPv6 address.

## Slide 3: The Format of an IPv6 address(cont’d..)
An IPv6 address is 128-bit long and uses 8 groups of 4 hexadecimal digits separated by colons. An IPv6 address looks like this:
FE80:0A3B:0002:4B3C:0F6D:3D40:FFC5:005A
Let’s now see:

## Slide 4: How to shorten an IPv6 address.
We have 2 rules of doing this:
Rule #1: A leading zero can be omitted.
For example, consider the following IPv6 address:
FE80:0A3B:0002:4B3C:0F6D:3D40:FFC5:005A
By omitting all leading zeros (in blue) , the address shortens to:
FE80:A3B:2:4B3C:F6D:3D40:FFC5:5A

## Slide 5: The Format of an IPv6 address(cont’d..)
2002:0000:0000:A29F:7D12:5502:63AF:BD2C
Replace the successive groups of zeros (in red) by double colon, and the shortened version will look like this:
2002::A29F:7D12:5502
What if now you were told shorten this address:
2002:0000:0000:2B3C:0000:0000:0000:55DA
Will the shortened version look like this-> 2002::2B3C::55DA ? NO!

## Slide 6: Cont’d…
Instead, the shortened version should either be 2002:0:0:2B3C::55DA or look like 2002::2B3C:0:0:0:55DA.
Why is this so? You can’t have more than one occurrence of a double colon in the shortened version because if you had, you wouldn’t know how many sets of zeroes were being omitted for each part. That’s the reason! You’ve seen it?
Moving on,
:002C
Shortened version– FF02:0:3D12::63AF:2C

## Slide 7: Cont’d..
We can always combine the two rules where applicable, so as to obtain the shortest address possible.
Quiz yourself: Test your understanding with these four:
1. Long version – 2002:0000:3D12:25AF:2788:00AB:63AF:002C
Shortened version– 2002:0:3D12:25AF:2788:AB:63AF:2C
2. Long version – FF02:0000:3D12:0000:0000:0000:63AF

## Slide 8: Cont’d..
3.Long version – FE80:A29F:0000:0000:4B2C:0000:0000:45DB
  Shortened version – FE80:A29F:0:0:4B2C::45DB
  Alternatively, the shortened version can be FE80:A29F::4B2C:0:0:45DB
4.Long Version – 2002:0000:0000:2B3C:0000:0000:0000:55DA
  Shortened version– 2002:0:0:2B3C::55DA
  Shortened version could also be – 2002::2B3C:0:0:0:55DA

## Slide 9: . IPv6 address types
In IPv4,
  3 types of addresses: unicast, multicast and broadcast.
In IPv6, broadcast addresses have been eliminated and replaced with anycast, unicast and multicast addresses.
  Unicast address – Identifies a single interface. Packets addressed to a unicast address are delivered to a single interface.
  Multicast address – Identifies a specific group of hosts. Just as for IPv4, packets sent to a multicast address are delivered to all interfaces identified by the multicast address. Multicast IPv6 addresses always start with FF.
  Anycast address– Like a multicast address, an anycast address identifies multiple interfaces, but there’s a difference: packets sent to an anycast address are delivered to one address- the address which is nearest to the source in terms of routing distance.
For example, we can assign the same anycast address to servers that offer a similar service. Packets sent to that IP address will be forwarded to the nearest server. For that reason, you can call an anycast address a ‘one-to-one-of-many‘ address. Anycast addresses are used for load balancing.

## Slide 10: Types of IPv6 unicast addresses
IPv6 unicast addresses are of three types:
Global unicast– These are publicly routable IPv6 addresses similar to public IPv4 addresses.
  They start with 2000::/3.
Link local -These are similar to IPv4 addresses in the Automatic Private IP Addressing (APIPA) range. These addresses are usable only within a network segment that a host is connected to.
  Routers will not forward packets destined to a link-local address to other links.
  A link-local address must be assigned to every network interface on which IPv6 protocol is enabled. These addresses with the prefix FE80::/10
Unique local – These have the same functions as private addresses in IPv4: to allow communication throughout a network segment while being routable to multiple local networks.
  Unique local addresses begin with the prefix FD00::/8.
Note: Before you can use IPv6 addressing on a router, always remember to first enable IPv6 routing on a router using the IPv6 unicast-routing command from its global configuration mode.